## Slide 1: EnerNOC Customer Data Presentation July 13, 2016

## Slide 2: What Problem Needs to Get Solved?
Currently vendors need to install a pulse output on a utility meter in order to help C&I customer manage energy usage in near real-time
The cost of this installation and ongoing maintenance and connectivity can be thousands of dollars per customer site, making it cost prohibitive to work with smaller customers, and the market less attractive for end-use customers and vendors
Demand response settlement can be an extremely time-consuming, manual process, which requires retrieving data through outdated means

## Slide 3: Customer Data Use Cases
Demand response settlement: Accuracy (+-2%) and accessibility are key. Need to download data from utility website in an automated, quick fashion (Green Button Connect My Data).
Demand response “coaching” during events: Latency (15 minute) and granularity (5 minute) are most important. Need to give customer insight into performance in a time frame where they can still take action. Accessibility also necessary either through HAN or AMI backhaul
Real-time energy management: Latency (15 minute) and granularity (5 minute) are most important. If customer wants peak demand alert, need data as close to interval as possible
DER dispatch/settlement for wholesale purposes: Five-minute latency may become necessary as DER is used for ancillary or other fast-acting grid support services.

## Slide 4: Process Issues
DSPs need to ensure that monthly usage and peak from AMI interval data is within 2% accuracy of monthly billed usage and peak.
Accuracy anomalies issues should be resolved within one month of identification, and DSPs should provide monthly reporting indicating the prevalence of anomalies, the status of maintenance activities, and root cause analysis results.
Documentation should be made available explaining how interval data will be collected, processed, and used for various applications including billing, real-time grid management, and third-party. Important considerations include, but are not limited to, a) whether the data used for billing is the same as what would be available via near-real time backhaul, b) any pre- or post-collection processing that occurs c) anomaly/error detection and correction (VEE) location
An interface should be provided to access data “as-of” a specific time to understand how a specific reading may have changed due to post-processing, VEE, etc and what the error was. When a customer’s data changes, an update should be pushed with well-documented metadata to allow third-party service providers to appropriately represent the state of this data.

## Slide 5: Lessons Learned from Other Jurisdictions
Include a budget for operational support and training for utility staff around AMI metering technology. Staff should be able to field questions from customers and their third parties.
Related to HAN/BAN, enable the meter radio prior to roll-out. Many utilities haven’t, driving up costs. HAN/BAN becomes less critical if data is backhauled with sufficiently low latency
Also for HAN/BAN, standardize and streamline device certification. Currently, device manufacturers face a myriad of certification requirements. Utilities should recognize an existing standard (such as UL) or band together to create a common standard.
Use a widely accepted and supported technology such as Zigbee, and avoid proprietary communication protocols/ technologies. Develop a simple device pairing and provisioning process (web form) between the gateway device and the meter